CONFINED SPACE ENTRY PROGRAM

General Industry Standard 29 CFR 1910.146

Prepared for:

(INSERT YOUR AGENCY HERE)

Reviewed by (print name):  ________________________________

Signature:______________________________________________ Date: __________

TABLE OF CONTENTS

PURPOSE	1

SCOPE	1

DEFINITIONS	1

RESPONSIBILITIES	4

PROCEDURES	6

Permit Procedures	6

Entry Permit Systems	6

Pre-Entry Procedures	7

Evaluation of Permit Space Atmospheric Conditions	7

Entry into Confined Spaces having Unacceptable Environmental Conditions	9

Work Activities in Permit-Required Confined Spaces	9

Concluding Entry Operations	10

Entry Operations by more than One Employer	10

Alternate Entry Procedures	10

Reclassification Entry Procedures	10

Temporary Reclassification	11

Non-Permit Required	11

Manhole Entry Procedures	11

SUBCONTRACTORS	12

RESCUE AND EMERGENCY SERVICES	13

TRAINING	14

PROGRAM EVALUATION	15

APPENDIX A – LIST OF PERMIT REQUIRED CONFINED SPACES	16

APPENDIX B - LIST OF NON-PERMIT CONFINED SPACES	17

APPENDIX C – CONFINED SPACE ENTR EQUIPMENT	18

APPENDIX D - CONTRACTOR REVIEW OF CONFINED SPACE ENTRY PROGRAM	19

This program can be developed for a municipality, a utility or housing authority, or a department.  NJPEOSH does not specify how the program must be organized.  It is the employer’s decision how to best organize the Program: city-wide, for the authority as a whole, or by department.

----------REMOVE ABOVE PARAGRAPH----------

## PURPOSE

This program identifies the confined spaces and permit-required confined spaces at the INSERT AGENCY’S NAME.

This program establishes the minimum requirements, including a permit system, for safe entry and work in permit-required confined spaces in accordance with the requirements of OSHA's Permit-Required Confined Spaces Standard (29 CFR 1910.146).

This program also identifies those individuals who play an active role in the entry of permit spaces, the types of equipment required to conduct entry operations and requirements for contractors who enter permit spaces at this facility.

## SCOPE

This program will apply to all employees of INSERT AGENCY’S NAME and external support personnel (i.e., contractors) who are required to enter, attend or conduct air sampling in any permit-required confined space at this facility.

A confined space has limited or restricted means of entrance or exit, is large enough for an employee to enter and perform assigned work, and is not designed for continuous occupancy by the employee.  For the purposes of INSERT AGENCY’S NAME employees, confined space include

- Manholes

- metering chambers

- wet well

- valve chambers

- pump stations

- grease pits and sewer trenches,

- and any other spaces that have direct contact with wastewater, sewage or sludge gas.

Non-permitted, alternate entry procedures and re-classifications are also defined in this program.

A permit required confined space meets the definition of a confined space and has one or more of the following characteristics:  (1) Contains or has the potential to contain a hazardous atmosphere, (2) contains a material that has the potential for engulfing an entrant, (3) has an internal configuration that might cause an entrant to be trapped or asphyxiated by inwardly converging walls or by a floor that slopes downward and tapers to a smaller cross section, and/or (4) contains any other serious safety or health hazards.

The confined space permit identifies the actual and potential hazards reasonably expected to be associated with the confined space at the time of entry.

## DEFINITIONS

As part of the final Permit-Required Confined Spaces Standard, OSHA has defined certain terms that are crucial to understanding the Standard.  The following are just a few of the key terms, along with their definitions, that will help to better understand this Confined Space Entry Program:

Acceptable Entry Conditions are the conditions that must exist in a permit space to allow entry and to ensure that employees involved with a permit-required confined space entry can safely enter into and work within the space.

Attendant is an individual stationed outside one or more permit spaces who monitors the authorized entrants and who performs all attendant’s duties assigned in the employer’s permit space program.

Authorized Entrant is an employee who is authorized by the employer to enter a permit space.

Confined Space is a space that:

- Is large enough and so configured that an employee can enter and perform assigned work;

- Has limited or restricted means for entry or exit (for example, tanks, vessels, silos, storage bins, hoppers, vaults and pits are spaces that may have limited entry); and

- Is not designed for continuous employee occupancy.

Engulfment is the surrounding and effective capture of a person by a liquid or finely divided (flow able) solid substance.

Entry is the action by which a person passes through an opening into a permit-required confined space.  Entry includes ensuing work activities in that space and is considered to have occurred as soon as any part of the entrant’s body breaks the plane of an opening into the space.

Entry Permit (permit) is the written or printed document that is provided by the employer to allow and control entry into a permit space.

Entry Supervisor is the person (such as the employer, foreman or crew chief) responsible for determining if acceptable entry conditions are present in a permit space where entry is planned for authorizing entry and overseeing entry operations and for terminating entry as required by this section.

Hazardous Atmosphere is an atmosphere that may expose employees to the risk of death, incapacitation, impairment of ability to self-rescue, injury, or acute illness from one or more of the following causes:

- Flammable gas, vapor, or mist in excess of 10 percent of its lower flammable limit (LFL);

- Airborne combustible dust at a concentration that meets or exceeds its LFL (vision obscured at 5 feet or less);

- Atmospheric oxygen concentration below 19.5 percent or above 23.5 percent;

- Atmospheric concentration of any substance which exceeds OSHA’s Permissible Exposure Limit (PEL); and

- Any other atmospheric condition that is immediately dangerous to life or health.

Hot Work Permit is the employer’s written authorization to perform operations (i.e., riveting, welding, cutting, burning and heating) capable of providing a source of ignition.

Immediately Dangerous to Life or Health (IDLH) is any condition that poses an immediate or delayed threat to life or that would cause irreversible adverse health effects or that would interfere with an individual’s ability to escape unaided from a permit space.

Isolation is the process by which a permit space is removed from service and completely protected against the release of energy and material into the space by such means as:  blanking or blinding; misaligning or removing sections of lines, pipes or ducts; a double block or bleed system; lockout or tagout of all sources of energy or blocking or disconnecting all mechanical linkages.

Non-Permit Confined Space is a confined space that does not contain or, with respect to atmospheric hazards, have the potential to contain any hazard capable of causing death or serious physical harm.

Oxygen Deficient Atmosphere is an atmosphere containing less than 19.5 percent oxygen by volume.

Oxygen Enriched Atmosphere is an atmosphere containing more than 23.5 percent oxygen by volume.

Permit-Required Confined Space (or permit space) is a confined space that has one or more of the following characteristics:

- Contains or has a potential to contain a hazardous atmosphere;

- Contains a material that has the potential for engulfing an entrant;

- Has an internal configuration such that an entrant could be trapped or asphyxiated by inwardly converging walls or by a floor which slopes downward and tapers to a smaller cross-section; or

- Contains any other recognized serious safety or health hazard.

(See Appendices A and B for a list of confined spaces that have been identified.)

Permit-Required Confined Space Program is the employer’s overall program for controlling, and, where appropriate, for protecting employees from, permit space hazards and for regulating employee entry into permit spaces.

Permit System is the employer’s written procedure for preparing and issuing permits for entry and for returning the permit space to service following termination of entry.

Prohibited Condition is any condition in a permit space that is not allowed by the permit during the period when entry is authorized.

Rescue Service is the personnel designated to rescue employees from permit spaces.

Retrieval System is the equipment (including a retrieval line, chest or full-body harness, and a lifting device and anchorage) used for non-entry rescue of persons from permit spaces.

Testing is the process by which the hazards that may confront entrants of a permit space are identified and evaluated.  Testing includes specifying the tests that are to be performed in the permit space.

## RESPONSIBILITIES

Program Administrator

The INSERT JOB TITLE is responsible for the oversight of this Confined Space Entry Program and for the approval of any revisions to the procedures contained herein.

The INSERT JOB TITLE is responsible for providing/arranging worker training and for ensuring that the required equipment is available to safely enter permit-required confined spaces.

The INSERT JOB TITLE is responsible for implementing this Confined Space Entry Program, for ensuring that personnel follow the procedures described in this program, and for verifying that the required equipment is available to safely enter permit-required confined spaces.

Entry Supervisors

INSERT AGENCY’S NAME shall ensure that each Entry Supervisor:

- Knows the hazards that may be faced during entry.

  - Must be familiar with information on the mode signs or symptoms, and consequences of the exposure.

- Verifies:

  - That rescue services are available and that the means for contacting them is operable.

  - The appropriate entries have been made on the permit,

  - All tests specified by the permit have been conducted

  - All procedures and equipment specified by the permit are in place before endorsing the permit and allowing entry to begin.

- Terminates the entry and cancels the permits at the end of the shift or when conditions change.

- Removes unauthorized individuals who enter or who attempt to enter the permit space during entry operations.

Attendants

At least one attendant shall remain outside the permit space into which entry is authorized for the duration of entry operations.  There shall be a minimum of one attendant provided for each permitted entry operation, and an attendant may only monitor one permit space at a time.

The attendant shall also:

- Know the hazards that may be faced during entry, including information on the mode signs or symptoms, and consequences of the exposure.

- Is aware of the possible behavioral effects of hazard exposure in authorized entrants.

- Continuously maintain an accurate count of authorized entrants in the permit space.

- Maintain constant communication with the entrant(s) through visual, verbal, signal, or other equivalent means.

- Remain outside the confined space at all times unless replaced by another authorized attendant.

- Monitor activities inside and outside of the space to determine if it is safe for entrants to remain in the space and orders the authorized entrants to evacuate the permit space immediately under any of the following conditions:

  - If the attendant detects a prohibited condition;

  - If the attendant detects the behavioral effects of hazard exposure in an authorized entrant;

  - If the attendant detects a situation outside of the space that could endanger an authorized entrant; or

  - If the attendant cannot effectively and safely perform his/her duties.

- Summon Rescue and other emergency services as soon as the attendant determines that 	authorized entrants may need assistance to escape from permit space hazards.

- Take the following precautions when unauthorized persons approach or enter a permit space while entry is underway:

  - Warn the unauthorized persons that they must stay away from the permit space;

  - Advise the unauthorized persons that they must exit immediately if they have entered the permit space; and

  - Inform the authorized entrants and the entry supervisor if unauthorized persons have entered the space.

- Perform non-entry rescue as specified by INSERT AGENCY’S NAME established rescue procedures.

- Perform no other duties that may interfere with the attendant's primary duty to monitor and protect the authorized entrants.

Entrants

In addition to the requirements for attendants and entrants outlined in the "Work Activities in Permit-Required Confined Spaces", entrants shall:

- Know the hazards that may be faced with during entry, including information on the mode, signs, or symptoms, and consequences of the exposure.

- Maintain Communication

- Alert the attendant whenever;

- The entrant detects a change in conditions.

- The entrant detects a change in the atmosphere.

- Exit from the permit space as quickly as possible whenever;

- An order to evacuate is given by the attendant or the entry supervisor;

- The entrant detects a prohibited condition or change in atmosphere

- An evacuation alarm is activated.

- Conduct work activities safely in accordance with established guidelines, permits, and procedures.

## PROCEDURES

Policy

No one will enter a permit-required confined space unless a confined space entry permit has been completed and signed by a qualified person (i.e., entry supervisor).  Appendix A identifies all permit-required confined spaces in the INSERT AGENCY’S NAME. INSERT AGENCY’S NAME must inform all exposed employees, by posting danger signs or by any other equally effective means, of the existence and location of and the danger posed by the permit spaces.

## Permit Procedures

The Entry Supervisor shall be responsible for completing the confined space entry permit.  The entry permit will specify acceptable entry conditions for each permit space in the INSERT AGENCY’S NAME.

The Entry Supervisor must ensure that the atmospheric conditions are acceptable in accordance with the entry permit, follow the pre-entry isolation procedures required by the entry permit, and ensure that the protective clothing, ventilation equipment, and any other equipment required by the permit are available at the entry site.

## Entry Permit Systems

Before entry into permit-required confined spaces, the Entry Supervisor shall document the completion of the measures required for entry.  The Entry Supervisor identified on the permit shall sign the entry permit to authorize entry.

The completed permit shall be made available at the time of entry to all authorized entrants by posting it at the entry portal so that the entrants can confirm that pre-entry preparations have been completed.

The Entry Supervisor shall terminate entry and cancel the entry permit when the entry operations specified in the permit have been completed or when unacceptable conditions not listed on the entry permit arise in or near the space.

The duration of entry permits shall not exceed a single continuous shift as specified on the actual permit unless a special entry permit is issued for the duration of the job.

## Pre-Entry Procedures

Prior to entry into a confined space, the Entry Supervisor shall:

- Ensure the confined space is isolated and locked out/tagged out in accordance with OSHA’s

- Control of Hazardous Energy (Lockout/Tagout) Standard (29 CFR 191.147).

- Ensure that no significant pressure differential exists across the opening, no dangerous spillage occurs, and no harm to personnel occurs when the confined space is opened.

- When entrance covers are removed, the opening shall be promptly guarded by a railing,   temporary cover, or other temporary barrier that will prevent an accidental fall through the opening and that will protect each employee when working in the space from foreign objects entering the space.

- Ensure that emergency communication equipment or personnel are readily available for the attendant.  Specifically, telephone communication must be established between the designated response organization and the Entry Supervisor.

- Ensure that all requirements identified in Section I of the entry permit are implemented prior to the initial atmospheric testing of the space.

- Implement atmospheric testing and monitoring procedures in accordance with Section II of the entry permit.

## Evaluation of Permit Space Atmospheric Conditions

The following procedures will be followed to evaluate atmospheric conditions in permit spaces before entry operations are conducted:

Test conditions in the permit space to determine if acceptable entry conditions exist;

- before entry is authorized to begin, and

- before ventilation equipment is installed, except that,

  - if isolation of the space is infeasible because the space is large or part of a continuous system (such as a sewer), pre-entry testing shall be performed to the extent feasible before entry is authorized.

- if entry is authorized, entry conditions shall be continuously monitored in the areas where authorized entrants are working.

Test and monitor the space prior to opening and continuously to determine if acceptable entry conditions are being maintained during the course of entry operations.  Procedures for testing and monitoring of atmospheric conditions in confined spaces are listed below.

When testing for atmospheric hazards,

- first test for oxygen,

- then for flammable/combustible gases and vapors,

- then for toxic gases or vapors.

Initial testing of atmospheric condition are as follows:

- Air sampling shall be performed by a qualified individual.

- All appropriate procedures shall be followed when using air-sampling equipment.

- Air sampling shall be performed so as to obtain a representative sample of the space.  This should be accomplished by using an approved extension hose or probe to obtain samples from the various levels/areas of the space.

- Initial sampling must be conducted at the top, middle and bottom ranges.  For spaces deeper than 12 feet, testing occurs at increments of 4 foot depths.

- The date, time, instrument number, air quality sample results, and initials of the individual conducting sampling shall be recorded in the appropriate boxes on the entry permit (Section II).

- If all conditions are acceptable based on the limits specified on the entry permit, the "Yes" box should be checked under the "Acceptable Environmental Conditions" section of the entry permit.

- If all conditions are not acceptable based on the limits specified on the entry permit, the "No" box should be checked under the "Acceptable Environmental Conditions" section of the entry permit.

- If the "No" box has been checked under the "Acceptable Environmental Conditions" section of the entry permit, the following steps shall be taken:

  - STOP

  - Notify the entry supervisor of the monitoring results.

  - If the space must be purged and ventilated, the supervisor must ensure that the requirements for ventilation of confined spaces are met.  (see "Work Activities in Confined Spaces")

  - An attendant shall be posted at the opening of the space to prevent unauthorized entry.  If no attendant is available, all work must cease.

  - If air sample results showed unacceptable flammability hazards, a sign shall also be posted with the following warning, "Danger-No Open Flames, Sparks, or Spark Generating Equipment within 50 feet".

9.	When air sampling meets acceptable entry conditions, the supervisor shall post a copy of the permit at the opening of the space and provide a copy of the permit to the entry attendant.

Upon initial entry into a permit space, atmospheric conditions must be monitored to ensure acceptable conditions. Procedures for continuous testing of the atmospheric conditions in confined spaces include the following:

- Continuous air monitoring will be performed until completion of any confined space entry.

- The continuous monitoring results shall be recorded on the entry permit at the intervals specified on the permit.

- If at any time, monitoring results exceed the acceptable limits specified on the entry permit, the supervisor or attendant shall instruct all entrants to exit the space immediately.

## Entry into Confined Spaces having Unacceptable Environmental Conditions

Employees of the INSERT AGENCY’S NAME will not enter permit-required confined spaces which exhibit unacceptable environmental conditions.  The entry permit shall determine acceptable entry conditions for each specific permit space.

If conditions in a permit space change during entry operations and conditions become unacceptable in accordance with the entry permit, entrants will be ordered to exit the space immediately.  The cause of the unacceptable environmental conditions will then be determined by the entry supervisor, and the procedures outlined in this plan for the "reviewing entry operations" will be utilized.

## Work Activities in Permit-Required Confined Spaces

The entry supervisor shall ensure that the entry permit is posted at the opening of the confined space.

Prior to entry into a confined space, the attendant and all entrants shall be briefed on all sections of the permit.

The attendant and all entrants shall ensure that the air quality has been tested within the periods specified on the permit and that the "yes" box under the "Acceptable Environmental Conditions" has been checked.  There shall be no hazardous atmosphere within the space whenever employees are in the space.

Hot-work will be performed by INSERT AGENCY’S NAME employees in confined spaces only upon completion of a Hot-Work Permit.

When electric power tools or equipment are used in confined spaces, the following guidelines apply:

- Electric power tools or equipment shall not be used in a potentially flammable atmosphere unless approved for such use.

- Electric power tools shall not be used in wet confined spaces unless equipped with a ground-fault circuit interrupter.

When ventilation is required in permit spaces, the following requirements will be followed:

- Continuous forced air ventilation shall be used until the forced air ventilation has removed any hazardous atmosphere.

- The forced air ventilation shall be so directed as to ventilate the immediate area where an employee is or may be present within the space and shall continue until all employees have left the space.

- The air supply for the forced air ventilation shall be from a clean source and may not increase hazards in the space.

- Ventilation equipment must be capable of producing 4 air changes per hour.

## Concluding Entry Operations

When entry operations are complete, all appropriate steps will be taken to close off the permit space.  The supervisor shall ensure that all debris, tools, and chemicals are cleaned up and removed from the confined space.

All permits shall be canceled by the Entry Supervisor upon completion of entry operations and closing off the permit space.

The canceled permit(s) shall be kept on file for a minimum of one year.

## Entry Operations by more than One Employer

When entry operations occur at the INSERT AGENCY’S NAME, Outside Contractors authorized entrants will be the employees of one employer only.  During no permitted entry operation (this excludes emergency rescue services) will employees from more than one employer be authorized to enter the space at the same time.

If employees of one employer are to perform entry operations in a permit space, all other employees (including contractors and INSERT AGENCY’S NAME employees) who will be conducting work in the area of that permit space shall be made aware that permit entry is occurring, and that precautions may need to be taken to protect authorized entrants.

## Alternate Entry Procedures

OSHA allows employers to use an alternate entry procedure for permit spaces where the only hazard is atmospheric, and continuous forced air ventilation alone can control the hazard.  Entrance into this space still requires continuous monitoring documented on the permit.  By using the alternate procedure, employers are able to simplify confined space entries by eliminating OSHA’s requirements for:

- An attendant during the entry, a written permit and emergency rescue provisions.  If any other hazard other than atmospheric exist, qualifying as an alternate space is not applicable.

- Other hazards are limited or restricted means of access or egress, engulfment, possibility of IDHL atmosphere, changing conditions.  Refer to pages 1- 3 of OSHA Standard 1910.146, included as attachment of this manual.

## Reclassification Entry Procedures

When a permit space poses no actual or potential atmospheric hazards and if all hazards within the space are eliminated without entry into the space, the permit space may be reclassified as a non-permit confined space.

All entrants must exit a declassification space immediately if any hazards become present.  Following evacuation, the space has to be re-evaluated as to whether it should be reclassified as a permit space again.  When a permit space is reclassified, the employer must document the cause for determining that all hazards have been eliminated.  Documentation needs to include the date, location of space and the signature of the person making the reclassification determination, and copy of the hazard analysis form.

## Temporary Reclassification

Temporary reclassify a permit required for confined space based on control or elimination of hazards.  Documentation regarding the reclassification must be included on the permit.  The reclassification may be changed from permit to non-permitted.  A permit space reclassification form must be filled out before area is considered safe for entry.

## Non-Permit Required

Hazards must be eliminated prior to entry without entering.  Document hazard control or elimination.  Assume hazards are present until hazard assessment and applicable controls are completed.

## Manhole Entry Procedures

Sewerage manholes must frequently be entered for inspection, rehabilitation purposes, stoppages, and removal of debris.  This program provides guidelines for safe entry and exit from the system.  Additionally, Work Zone training will be required for employees who work with manholes.

Before time of entry into a manhole the Entry Supervisor shall review procedures and discuss the job to be executed.  The rescue service shall be alerted and prepared in the event of an emergency.  The appropriate traffic safety measures shall be instituted, then the following step conducted.

- Complete Confined Space Entry Permit.

- Test manhole atmosphere with portable gas detector.  Lower meter through entire length of manhole & record results.

- If readings are in the specified range - proceed to the next step.  If not, ventilate and retest.  If ventilation fails to clear the hazardous atmosphere, DO NOT ENTER the manhole.  Notify the Supervisor for further instructions.

- Smell air for unusual odors (waft air with hand).  If any unusual odors are present ventilate and recheck.  If strong odors continue, DO NOT ENTER.  Notify Supervisor.

- Set up the tripod unit.  Install manhole guard around the entrance with posted sign “Confined Space Permit Required”.

- Secure harness and life-line on the employee entering manhole, check and make sure that all protective equipment is on - duty of the trained attendant.

- Enter manhole with gas detection equipment.  If the detection equipment shows a hazardous atmosphere at any point EXIT IMMEDIATELY.

- Stand by crew must make sure all lines are secure.

- Maintain communications - entrant shall continuously notify the attendant of his actions.  Perform job and exit carefully.

## SUBCONTRACTORS

When a contractor is hired by INSERT AGENCY’S NAME to perform work that involves permit space entry, the following requirements shall be met by the facility:

- Inform the contractor that the facility contains permit spaces and that permit space entry is allowed through a written confined space entry program that fulfills the requirements of 29 CFR 1910.146, Permit-Required Confined Spaces.

- Apprise the contractor of the hazards posed by the confined spaces that make the space a permit space.

- Apprise the contractor of any precautions or procedures that the facility has implemented for the protection of employees in or near permit spaces where contractor personnel will be working.

- Meet with the contractor after entry operations regarding the entry and regarding any hazards confronted or created in permit spaces during entry operations.

- Coordinate entry operations when employees of more than one contractor are working simultaneously as authorized entrants in or near a permit space (i.e., two or more contractors), so that employees of one employer do not endanger the employees of any other employer.  However, it is the policy of INSERT AGENCY’S NAME that only employees of one contractor may enter a permit space at one time.

Contractors who perform permit space entry operations shall:

- Comply with the requirements for confined space entry outlined in the OSHA Permit-Required Confined Spaces Standard, 29 CFR 1910.146.  This includes providing documentation that employees have received education and training for entry into confined spaces, a written confined space entry program, and a permit system.

- Provide personnel, or make arrangements to provide, rescue and emergency response services. If the contractor will perform rescue and emergency services, they must provide documentation that employees have been trained to perform confined spaces rescue and emergency operations, and the contractor must physically provide all necessary equipment that may be required in the event of an emergency rescue situation before entry operations proceed. Obtain any available information regarding the permit space hazards and entry operations from INSERT AGENCY’S NAME coordinate entry operations with INSERT AGENCY’S NAME Confined Space Team when INSERT AGENCY’S NAME employees and contractor personnel will be working in or near permit spaces.

- Inform INSERT AGENCY’S NAME Confined Space Team of the permit space program that the contractor will follow and of any hazards confronted or created in permit spaces.

- If any unexpected, non-permitted hazards arise during entry operations, the contractor shall stop entry operations and exit the space.  INSERT AGENCY’S NAME, or his/her representative, shall be made aware of the situation immediately.

## RESCUE AND EMERGENCY SERVICES

Confined Space Entry Rescue

INSERT AGENCY’S NAME shall provide Confined Space Rescue Services, through the Responsible Entry Team, at the INSERT AGENCY’S NAME for emergency situations.

Before any entry into a permit space, the Entry Supervisor shall verify that communication is available between the INSERT AGENCY’S NAME/Outside Contractors and the Confined Space Entry Rescue Team.  Arrangements must be made before entry operations to allow for immediate contact between the INSERT AGENCY’S NAME/Outside Contractors and the Confined Space Entry Rescue Team.

The arrangement shall be accomplished by contacting the Confined Space Entry Rescue Team on the day of the scheduled entry and informing them that a confined space entry is scheduled for this shift.  The Confined Space Entry Rescue Team will inform the INSERT AGENCY’S NAME / Outside Contractors at this time if the Confined Space Entry Team is available.

If the possibility exists that the Confined Space Rescue Team may be called to provide rescue services for other facilities as a INSERT AGENCY’S NAME confined space entry is in progress.  All entry operation ceases. The confined space entry will be cancelled and rescheduled for a later time.

Non-Entry Rescue

To facilitate non-entry rescue, retrieval systems or methods shall be used whenever an authorized entrant enters a permit space, unless the retrieval equipment would increase the overall risk of entry or would not contribute to the rescue of the entrant.  Retrieval systems shall meet the following requirements:

- Each authorized entrant shall use a chest or full body harness with a retrieval line attached at the center of the entrant's back near shoulder level, or above the entrant's head.

- A mechanical device shall be available to retrieve personnel from vertical permit spaces more than 5 feet deep.  If during the course of a permit space entry, an attendant becomes aware that an entrant needs assistance escaping from the confined space hazards, the attendant shall; summon rescue and begin Non-Entry Rescue Procedures.

- The retrieval line shall be attached to a mechanical device or fixed point outside the permit space in such a manner that rescue can begin as soon as the rescuer becomes aware that rescue is necessary.  Retrieval equipment must have a 4 to 1 mechanical advantage.

Emergency Procedures

All entrants shall immediately exit the confined space at the first indication of any hazard to their safety.  These indications include, but are not limited to, the following:

- Dizziness, fatigue, confusion, headaches, nausea, etc.

- Chemical spills or discharges in the space.

- Fire or explosion.

- Alarms

- Any other serious safety or health hazard.

All entrants shall immediately exit the space if instructed to do so by the attendant or the entry supervisor.

If an entrant becomes incapacitated in the confined space, other entrants exposed to similar hazards in the space shall exit the space immediately.

In the event of an emergency, the attendant shall:

- Report the emergency by telephoning 911 or designated emergency number.

- Provide all information necessary for appropriate response organizations, (i.e., the local Fire Department).

Under no circumstance shall any INSERT AGENCY’s NAME /Outside Contractor attempt to enter a confined space to perform a rescue.  The Rescue Team shall handle all rescue operations that require entry into the confined space.

## TRAINING

Each employee serving as authorized entrant, attendant, entry supervisor, during any type of confined space operation, shall be trained so that they have the understanding, knowledge, and skills necessary for the safe performance of their duties.  This training shall include the following:

- The operation of the permit system.

- The specific duties of each person involved in permit space operations.

- The hazards of confined spaces including information on the mode, signs or symptoms, and consequences of exposure.

- The proper use of equipment required during permit space operations including:  testing and monitoring equipment, ventilation equipment, communication equipment, personal protective equipment, lighting equipment, barriers and shields, ingress/egress equipment, rescue and emergency equipment used for non-entry rescue, and any other equipment necessary for safe entry into and rescue from permit spaces.

- The importance of communication between entrants and attendants.

- The conditions under which a confined space should be evacuated.

- The procedures for summoning rescuers.

- The procedures to be used for rescue.

Training shall also be provided to each affected employee:

- Before the employee is first assigned permit space operations duty.

- Before there is a change in assigned duties.

- Whenever there is a change in permit space operations that presents a hazard about which an employee has not previously been trained.

- Whenever the facility has reason to believe either that there are deviations from the permit space entry procedures or that there are inadequacies in the employee's knowledge or use of these procedures.

The training shall establish employee proficiency in the duties required of authorized entrants, attendants, entry supervisors, and members of the in-plant rescue team, and shall introduce new or revised procedures, as necessary.

Once trained, each employee serving as an authorized entrant, attendant or entry supervisor shall be certified.  The certification shall include the employee's name, the name of the trainer, and the date of training.  The certification shall be available for inspection by employees and their authorized representatives.

## PROGRAM EVALUATION

This Confined Space Entry Program shall be evaluated annually.  The canceled permits that are retained shall be used to assist in the review of the program.  The annual review should also include a review of all entry and pre-entry procedures, and interviews with all authorized entrants, attendants, and supervisors.

The results of the program review and evaluation will be made available to employees and presented to senior management of the INSERT AGENCY’S NAME in order to implement recommended adaptations.

# APPENDIX A – LIST OF PERMIT REQUIRED CONFINED SPACES

| Confined Space | Location | Hazard(s) | Rescue Plan |
| --- | --- | --- | --- |

# APPENDIX B - LIST OF NON-PERMIT CONFINED SPACES

| Confined Space | Location | Last Trained | Last Evaluation |
| --- | --- | --- | --- |

# APPENDIX C – CONFINED SPACE ENTR EQUIPMENT

| Equipment | Maintenance Procedure | Last Tested |
| --- | --- | --- |

# APPENDIX D - CONTRACTOR REVIEW OF CONFINED SPACE ENTRY PROGRAM

On INSERT DATE I received a copy of the INSERT CONTRACTOR COMPANY Confined Space Entry Program and reviewed them with the INSERT AGENCY’S NAME representative.  All work performed by personnel in our employment shall at a minimum conform to these procedures.

Contractor Name and Representative            INSERT AGENCY’S NAME REPRESENTATIVE

____________________________			________________________

____________________________			________________________